1.	A WORKING INTRODUCTION TO SHIFT-REDUCE PARSING

The shift-reduce parser is essentially a push down automaton. Hence it consists of a finite state machine with a stack. The stack is used to hold terminal and/or non-terminal symbols. The following is a gentle introduction to shift-reduce parsing.

Let us make the following assumptions:
- The input to be parsed, which is a sequence of terminal symbols is stored in an input buffer
- $ is used as an end-marker to mark the end of the input buffer and the stack.
- Once a terminal has been read from the input, it is removed from the input buffer.

Consider the following context free grammar:

(1)	expr :	expr '+' expr
(2)	|	'(' expr ')'
(3)	|	'0' | '1' |	'2' | '3' | '4' | '5' | '6' | '7' | '8' | '9'
(4)	;

The terminal set is {+,(,),0,1,2,3,4,5,6,7,8,9}. The only non-terminal is 'expr'.

Before the parsing process begins, the contents of the stack and the input buffer would be as follows:

STACK:	$	I/P BUFFER:	2 + 2 $

That is, the stack is initialized with the $ symbol. The input buffer is initialized with the input terminated by a $. In this example, 2+2 is the input to be parsed.

The contents of the stack and the contents of the input buffer together define the configuration of the parser.

On successful completion of parsing, the configuration would be:

STACK:	$ expr	I/P BUFFER:	$

where expr is the start variable of the parser's context free grammar i.e., at the end of successful parsing, the start symbol of the grammar followed by $ will appear on the stack whereas, the input buffer will contain nothing except the $.

At each step of parsing, the parser takes an action (the notion of action will be explained later) resulting in a configuration change. For our example, the following table shows the step-by-step change in the parser's configuration after each action taken by parser.

STACK	|	I/P BUFFER	|	ACTION TAKEN
----------------------------------------------------------------------------------------------------------------------------
(1)	$	|	2 + 2 $	|	_

(2)	2 $	|	+ 2 $	|	SHIFT

(3)	expr $	|	+ 2 $	|	REDUCE

(4)	+ expr $	|	2 $	|	SHIFT

(5)	2 + expr $	|	$	|	SHIFT

(6)	expr + expr $	|	$	|	REDUCE

(7)	expr $	|	$	|	REDUCE

(8)	expr $	|	$	|	ACCEPT

A shift-reduce parser can take four possible actions:

1. Shift is an action of shifting the next unread terminal from the input buffer to the stack. Once an input character is read, it is removed from the buffer and it is pushed onto the stack.

2. Reduce is an action of replacing one or more grammar symbols from the top of the stack that matches a body (right hand side) of a production, with the corresponding production head (left hand side). The contents on top of the stack which matches the right side of a production is called a handle. The process of replacing a handle with the corresponding production head is called reduction.

3. Accept is an action indicating that the entire input has been parsed successfully. The parser executes an accept action only if the input buffer is empty and the stack consists of the start variable alone. The stack or input buffer is said to be empty when the stack consists of the $ symbol alone, i.e. :

STACK:	$ <start_variable>	I/P BUFFER:	$

4. Error is an action indicating that an error was encountered while parsing the input. In our example, there was no error. We will see error conditions later.

EXPLANATION:

At each step of parsing, the shift-reduce parser decides on an action depending on the configuration of the parser. This decision making is achieved using predictive parsing. We will NOT investigate the process of predictive parsing in this documentation.

Let us revisit the actions taken in the above table.

(1)	STACK:	$	I/P BUFFER:	2 + 2 $

At this configuration, the parser executes a shift action i.e. 2 is pushed onto the stack resulting in the configuration:

(2)	STACK:	$ 2	I/P BUFFER:	+ 2 $

At configuration (2), the parser executes a reduce action as the contents on top of the stack match the body of the production expr -> '2' i.e., 2 is the handle in this case and a reduction takes place replacing the handle with the production head expr.

(3)	STACK:	$ expr	I/P BUFFER:	+ 2 $

Following the reduction, the parser shifts '+' to the stack.

(4)	STACK:	$ expr +	I/P BUFFER:	2 $

The parser shifts once again, resulting in the configuration:

(5)	STACK:	$ expr + 2	I/P BUFFER:	$

The parser executes a reduce action reducing the handle '2' to the grammar symbol expr.

(6)	STACK:	$ expr + expr	I/P BUFFER:	2 + 2 $

The handle expr + expr is further reduced to expr.

(7)	STACK:	$ expr	I/P BUFFER:	$

Since the I/P BUFFER is empty and the stack contains only the start variable, the parser executes an accept action, indicating that the input has been parsed successfully.

2.	CONFLICTS

A shift-reduce parser cannot be used to successfully parse all context free languages. Conflicts arise when the parser is unable to make a decision on the action to execute. These conflicts are practically of two-types: shift/reduce conflict and reduce/reduce conflict.

2.1	shift/reduce conflict

When the parser cannot decide whether to shift or to reduce in a configuration where both the actions seem to be viable options.

Example: The dangling else problem

Consider the following grammar:

statement	:	if boolean then statement
|	if boolean then statement else statement
|	stmt

boolean	:	true
|	false

And the following input:

if true then if false then stmt else stmt

When the parser is in the configuration:

STACK:	$ if boolean then if false then stmt
I/P BUFFER:	else stmt $

The parser cannot decide whether the contents on top of the stack is the handle. (Recall that a handle is a reducible string, i.e. A sequence of grammar symbols that matches the body of a production). The parser faces a conflict on deciding between the shift and reduce actions. This conflict is called shift/reduce conflict. In such a scenario, a shift as well as a reduce is possible (as shown below).

CASE 1: Parser decides to execute a shift

STACK:	$ if boolean then if false then stmt
I/P BUFFER:	else stmt $

ACTION:	shift
STACK:	$ if boolean then if false then stmt else
I/P BUFFER:	stmt $

ACTION:	shift
STACK:	$ if boolean then if false then stmt else stmt
I/P BUFFER:	$

ACTION:	reduce
STACK:	$ if boolean then stmt
I/P BUFFER:	$

ACTION:	reduce
STACK:	$ stmt
I/P BUFFER:	$

ACTION:	accept

In Case 1, the input

if true then if false then stmt else stmt

is interpreted as

if true then (if false then stmt else stmt)

CASE 2: Parser decides to execute a reduce

STACK:	$ if boolean then if false then stmt
I/P BUFFER:	else stmt $

ACTION:	reduce
STACK:	$ if boolean then stmt
I/P BUFFER:	else stmt $

ACTION:	shift
STACK:	$ if boolean then stmt else
I/P BUFFER:	stmt $

ACTION:	shift
STACK:	$ if boolean then stmt else stmt
I/P BUFFER:	$

ACTION:	reduce
STACK:	$ stmt
I/P BUFFER:	$

ACTION:	accept

In Case 2, the input

if true then if false then stmt else stmt

is interpreted as

if true then (if false then stmt) else stmt

An if-then-else statement “if boolean then stmt else stmt” is said to have a matched-then as it is followed by an else condition. An if-then statement “if boolean then stmt” is said to have a unmatched-then as it is not followed by an else statement. In Case 1, the else statement is associated with the nearest unmatched-then while in Case 2, the else statement is associated with the farthest unmatched-then.
The shift-reduce conflict arouse in above example because the grammar is an ambiguous grammar. (An ambiguous grammar is a grammar than can have more than one leftmost derivation for the same input). A shift-reduce parser cannot handle an ambiguous grammar. The class of context free grammars for which shift-reduce parsing can be used is called the LR(k) class. ( We will explore the LR(k) class of grammars later ).

2.2	reduce/reduce conflicts

When the parser cannot decide upon which of several possible reductions to make.

Example:

Consider the following grammar:

program	:	statement
|	conditional

statement	:	if boolean then stmt else stmt
|	stmt

conditional	:	if boolean then stmt else stmt
|	stmt

And the configuration to be:

STACK:	$ if boolean then stmt else stmt
I/P BUFFER:	$

The handle “if boolean then stmt else stmt” can be reduced using

statement	:	if boolean then stmt else stmt
or
conditional	:	if boolean then stmt else stmt

i.e., there are more than one possible reductions. The parser faces a conflict on deciding which of the several (two in this example) productions to reduce by. This conflict is called reduce/reduce conflict.