1	Introduction to YACC

YACC (Yet Another Compiler Compiler) is a tool used to generate a parser. This document is a tutorial for the use of YACC to generate a parser for SIL. YACC translates the Context Free Grammar (CFG) specifications (given as input in input_file.y) into a C implementation (y.tab.c) of a corresponding push down automaton i.e., a finite state machine with a stack. This C program when compiled, yields an executable parser.

YACC

y.tab.c
input_file.y

C compiler

a.out
y.tab.c

e
a.out

Output
Input

The source SIL program is fed as the input to the generated parser (a.out) which parses through the program and checks if the program can be derived from the CFG specification in the input_file.y file.

A parser is a program that parses through an input file to check if it is in accordance with a grammar specification. Parsing is the process of analyzing a string of symbols of a particular language (in this case SIL) according to the rules of a grammar specifications. The SIL syntax consists of precise rules that describe the structure of well formed programs in SIL. The syntax of SIL constructs can be specified by using Context Free Grammars in a YACC program.

Example:

grammar	:	variable = value	{printf(“ end ”);}
;

variable	:	'a'|'b'	{printf(“ variable ”);}
;

value	:	'0'|'1'	{printf(“ value ”);}
;

Sample Input/Output:

I:	a=1
O:	variable value end

I:	a=
O:	variable
syntax error

I:	s=5$
O:	syntax error

This example demonstrates the specification of rules in YACC. A rule in a YACC program comprises of two parts (i) the production part and (ii) the action part. In this example there are 3 production parts and 3 corresponding action parts. (Note that there are actually 5 productions and the latter 4 have been composed into 2 productions, hence resulting in 3 compact productions) Consider the first rule. This rule with the production head grammar (LHS of : ) specifies that when the parser has matched the given input with the body of the production (RHS of : ), it must execute the corresponding action (enclosed within {}).

Note: If the input does not match the grammar specification of the YACC generated parser, it will print an auto-generated “syntax error” message on the screen.

2.	The structure of YACC programs

A LEX program consists of three sections : Declarations, Rules and Auxiliary functions.

DECLARATIONS

%%

RULES

%%

AUXILIARY FUNCTIONS

2.1	Declarations

The Declarations sections of a YACC program consists of two parts, C declarations and YACC Declarations.

The C Declarations are delimited by %{ and %}. This part consists of all the declarations required for the C code written in the Actions section and the
 Auxiliary functions section. The contents of this section are directly copied into the generated y.tab.c file without any modification.

Example:

%{

#include<stdio.h>

%}

%token NUM

%%

expr	:	expr '+' expr
|	NUM

%%
/* Auxiliary functions */

The YACC Declarations consists of declarations of grammar tokens. In the above example NUM is a token. The token represents an input string which is obtained by calling yylex() (To be discussed in detail later). The tokens declared in this section are used in the Rules section.

2.2.	Rules