1	Introduction to LEX

LEX is a tool used to generate a lexical analyzer. This document is a tutorial for the use of LEX for SILC development. Technically, LEX translates a set of regular expression specifications (given as input in prog_file.l) into a C implementation of a corresponding finite state machine (lex.yy.c). This C program, when compiled, yields an executable lexical analyzer.

  LEX

lex.yy.c
prog_file.l

C compiler

a.out
lex.yy.c

e
a.out

Output

Input

The source SIL program is fed as the input to the the lexical analyzer which produces an output of a sequence of tokens. (Tokens are explained below).

Conceptually, a lexical analyzer scans a given source SIL program and produces an output of tokens. A token is a single element of the SIL programming language that is recognized by the compiler. For instance integer, boolean, begin, end, if, while etc. are tokens in SIL.

Example:

 “integer”	{return ID_TYPE_INTEGER;}

This example demonstrates the specification of rule in LEX. This rule in this example specifies that the lexical analyzer must return the token named ID_TYPE_INTEGER when the pattern “integer” is found in the input file. A rule in a LEX program comprises of a pattern part (specified by a regular expression) and a corresponding (semantic) action part (a sequence of C statements). In the above example, “integer” is the pattern and {return ID_TYPE_INTEGER;} is the corresponding action. The statements in the action part will be executed when the pattern is detected in the input.

2	The structure of LEX programs

A LEX program consists of three sections : Declarations, Rules and Auxiliary functions.

DECLARATIONS

%%

RULES

%%

AUXILIARY FUNCTIONS

2.1 Declarations

The declarations section consists of two parts, regular definitions and auxiliary declarations. LEX allows the use of short-hands and extensions to regular expressions for the regular definitions. The auxiliary declarations are copied as such by LEX to the output lex.yy.c file.

Example:

%{
#include<stdio.h>
int global_variable;	//Auxiliary declarations
%}
number	[0-9]+	//Regular definitions
op	[-|+|*|/|^|=]

%%
/* Rules */
%%
/* Auxiliary functions */

A regular definition in LEX is of the form :
D	R
where D is the symbol representing the regular expression R. The auxiliary declarations (which are optional) are written in C language and are enclosed within ' %{ ' and ' %} ' . It is generally used to declare functions, include header files, or define global variables and constants.

2.2 Rules

Rules in a LEX program consists of two parts :
1. The pattern to be matched
2. The corresponding action to be executed

Example:

/* Declarations*/
%%

{number}	{printf(“ number”);}
{op}	{printf(“ operator”);}

%%
/* Auxiliary functions */

The pattern to be matched is specified as a regular expression .

Sample Input/Output for the above example:

I: 234
O: number

I: *
O: operator

I: 2+3
O: number operator number

LEX obtains the regular expressions of the symbols number and op from the declarations section and generates code into a function yylex() in the lex.yy.c file. This function checks the input stream for the first match to one of the patterns specified and executes code in the action part corresponding to the pattern.

2.3 Auxiliary functions

LEX generates C code for the rules specified in the Rules section and places this code into a single function called yylex(). (To be discussed in detail later). In addition to this LEX generated code, the programmer may wish to add his own code to the lex.yy.c file. The auxiliary functions section allows the programmer to achieve this.

Example:

/* Declarations */
%%
/* Rules */
%%

int main()
{
yylex();
return 1;
}

The C code in the auxiliary section and the declarations in the declaration section are copied as such to the lex.yy.c file.
-------------------exercises to be added here ------------------
3	The yyvariables

The following variables are offered by LEX to aid the programmer in designing sophisticated lexical analyzers. These variables are accessible in the LEX program and are automatically declared by LEX in lex.yy.c.

- yyin
- yytext
- yyleng

3.1	yyin

yyin is a variable of the type FILE* and points to the input file - in this project, the SIL program file. yyin is defined by LEX automatically. If the programmer assigns an input file to yyin in the auxiliary functions section, then yyin is set to point to that file. Otherwise LEX assigns yyin to stdin(console input).

Example:

/* Declarations */
%%
/* Rules */
%%

main(int argc, char* argv[])
{
if(argc > 1)
{
FILE *fp = fopen(argv[1], “r”)
if(!fp)
yyin = fp;
}
}
yylex();
return 1;
}

Exercise:

In the generated lex.yy.c, the following code segment can be found under the definition of yylex().

if( ! yyin )
yyin = stdin;

Try to locate the above given code segment in the lex.yy.c and understanding the significance of it. (Reading machine generated code might be perplexing, in order to save time try searching the file.) What could be the consequences of removing this code segment from lex.yy.c before compiling it for generating the lexical analyzer?

The above statement indicates that if the programmer does not define yyin, then yylex() by default sets yyin to the console input. Hence, any re-definition for yyin must be made before invoking yylex(). (This will be explained in detail later).

3.2	yytext

yytext is of the type char* and it contains the lexeme currently found. A lexeme is a sequence of characters in the input stream that matches some pattern in the Rules Section. (In fact, it is the first matching sequence in the input from the position pointed to by yyin.)

yytext is initialized to NULL. Each invocation of the function yylex() results in yytext carrying a pointer to the lexeme found in the input stream by yylex().

NOTE: The programmer does not have to do any memory allocation for yytext as code for this is automatically generated by LEX.
[yytext points to the first character of the lexeme in the input buffer. The matched string is the part of the input buffer. The value of yytext will be overwritten after the next yylex() invocation.]

Example:

/* Declarations */
%%

{number}	{printf("Found : %d",atoi(yytext));}

%%

int main()
{
yylex();
return 1;
}

In the above example, if a lexeme is found for the pattern defined by number then corresponding action is executed . Consider the following sample i/o,

Sample Input/Output:

I: 25
O: Found : 25

In this case when yylex() is called, the input is read from the location given by yyin and a string “25” is found as a match to number. This location of this string in the memory is pointed to by yytext. The corresponding action in the above rule uses a built-in function atoi() to convert the string “25” (of type char*) to the integer 25 (of the type int) and then prints the result on the screen.

Exercise:

Suggest a modification in the above example to check whether a number found is even or odd.

3.3	yyleng

yyleng is a variable of the type int and it stores the length of the lexeme pointed to by yytext.

Example:

/* Declarations */
%%
/* Rules */
%%

{number}	printf("Number of digits = %d",yyleng);

Sample Input/Output:

I: 1234
O: Number of digits = 4

4	The yyfunctions

LEX provides the following functions to the programmer:
.
- yylex()
- yywrap()

4.1	yylex()

yylex() is a function of return type int. LEX automatically defines yylex() in lex.yy.c but does not call it. The programmer must call yylex() in the Auxiliary functions section of the LEX program. LEX generates code for the definition of yylex() according to the rules specified in the Rules section. When yylex() is invoked, it reads the input as pointed to by yyin and scans through the input looking for a matching pattern. When the input or a part of the input matches one of the given patterns, yylex() executes the corresponding action associated with the pattern as specified in the Rules section.
NOTE: yylex() stops scanning through the input once a pattern has been found or if the end of input has been encountered.

4.2	yywrap()
--------------------Add yywrap() description here---------------------------------------

5	The Even-Odd Program

%{
/*
1.Request input of an even and an odd number
2.indicate input characteristic : Even/Odd [digit_length]
3.check for input's correctness and print result
*/

#include<stdlib.h>
#include<stdio.h>

int number_1;
int number_2;
%}

number_sequence [0-9]*

%%

{number_sequence}[0|2|4|6|8]	{
printf("Even number [%d]",yyleng);
return atoi(yytext);
}

{number_sequence}[1|3|5|7|9]	{
printf("Odd number [%d]",yyleng);
return atoi(yytext);
}
%%

int yywrap
{
 return 1;
}

int main()
{
printf("\nInput an even number and an odd number\n");
 number_1 = yylex();
number_2 = yylex();
int diff = number_1 - number_2;
if(diff%2!=0)
printf("\nYour inputs were checked for correctness, \nResult : Correct\n");
else
printf("\nYour inputs were checked for correctness, \nResult : You do not know how to read\n");
return 1;
}

6	Disambiguation rules

LEX uses two important disambiguation rules in selecting the right action to execute in case of a conflict :
- Order of occurrence is assigned as the pattern's matching priority.
- “Longest match” is preferred.
Example :

   “break” { return BREAK; }
   [a-zA-Z][a-zA-Z0-9]* { return IDENTIFIER; }

Here, break is matched by both the regular expressions, but break is a keyword and not an identifier hence it is ordered in such a manner that LEX uses its first disambiguation rule to execute return BREAK;

Example :

/* Declarations section */
%%

“-”	{return MINUS;}
“--”	{return DECREMENT;}

%%
/* Auxiliary functions */

Assume that the function calling yylex() prints the name of the token.

Sample Input/Output:

I: -
O: MINUS

I: --
O: DECREMENT

I: ---
O: DECREMENT MINUS

Note that, in case of an –- input to the lexical analyzer, yylex() does not return two MINUS tokens, but instead returns a DECREMENT token, by the second disambiguation rule.

7	Pattern matching using LEX

Conceptually, LEX converts all its regular expressions into a finite state machine which it uses to accept or reject a string in the input stream. The corresponding action is executed when the machine is in accept state. The LEX compiler stores information about the constructed finite state machine in the form of a decision table (transition table) in the lex.yy.c file. Also the corresponding actions and the information regarding when they are to be executed is stored in the lex.yy.c file.
 A transition(current_state,input_char) function is used to access the decision table. LEX makes it's decision table visible if we compile the program with the -T flag. The finite state machine used by LEX is deterministic in nature i.e. it is a DFA. The simulation of the constructed DFA is done in the lex.yy.c file.
Hence, a LEX compiler constructs a DFA according to the specifications of the regular expression in the LEX program, and generates a simulation algorithm (to simulate the DFA) and a matching switch-case algorithm (to match and execute the appropriate action if the DFA enters an accept state).
8	The Token simulator program

%{
/* Scan and return a token for identifiers of the format :	(string)(number)
Note : strings are not case sensitive
examples : a0 , A1 , ab2 , AB4 , aBc5
*/
#include<stdio.h>

#define ID 1	//Identifier token
#define ER 2	//Error token

%}
low_case [a-z]
upp_case [A-Z]
number	[0-9]

%option noyywrap

%%
({low_case}|{upp_case})({low_case}|{upp_case})*({number})
return ID;
(.)*	return ER;

%%
int main()
{
int token = yylex();
if(token==ID)
printf("Acceptable\n");
else if(token==ER)
printf("Unacceptable\n");
return 1;
}
In this program, the main() function obtains the tokens (in place of a parser) and checks if the input contains a valid identifier.

Sample Input/Output:

I: Var9
O: Acceptable

When Var9 is provided as the input, the DFA constructed by LEX accepts the string, and the corresponding action return ID is found and executed. As a result yylex() returns the token ID, and the main() function prints Acceptable on the screen.

9	Construction of a DFA from a regular expression

The construction of a DFA from a regular expression takes place in two steps.
- Constructing a syntax tree from the regular expression
- Converting the syntax tree into a DFA

9.1	The intermediate syntax tree

Consider the first rule in the token simulator program in section 9. It consists of the following regular expression :
({low_case}|{upp_case})({low_case}|{upp_case})*({number})
For convenience in representation , it has been represented as :
( a | A ) ( a | A )* (N)
where, 'a' represents {low_case}, 'A' represents {upp_case} and 'N' represents {number}.
The syntax tree constructed for the above regular expression would look like :

º
    / \
 º N₅
      /	\
   |	*
       /	\	|
     a₁	A₂	|
     / \
        a₃ A₄

In the above figure º represents the 'cat' (concatenation) operator, * represents the 'star' operator (a unary operator) and | represents the 'or' operator. In the syntax tree the inner nodes are operators while the leaves are the operands. The subscript assigned to every leaf is called the position of the leaf. The position of a leaf plays a vital role in the process of constructing states for the DFA.

NOTE:
This syntax tree is an intermediate data structure. There will be no traces of this in lex.yy.c file, because it is only used in the construction of the DFA.

9.2	Constructing the DFA

Constructing the DFA involves two steps:
- Constructing the set of states of the DFA
- Constructing all the possible transitions made by the DFA from one state to another on different inputs.

The language represented by the regular expression ( a | A ) ( a | A )* (N), can only possibly start with an 'a' or 'A'. From the syntax tree we may infer that these could only correspond to positions 1 or 2 . Let the set of these positions {1,2} be the start state of the DFA. For convenience it has been named as state I.

Consider the position 1 ('a'), it could be followed by either of the positions 3,4 or 5. Let this be a new state {3,4,5} represented by II. The position 2 ('A') could be possibly followed by either of the positions 3,4 or 5. But a new state is not required as {3,4,5} has already been represented by II. Similarly the positions 3 and 4 could be followed by the position 3 or 4 or 5. If followed by 5, the DFA must accept and terminate (syntax tree ends at position 5). Hence let the final (accept) state be III.
Thus, the transitions maybe formulated as :

Current state	->	Input symbol	->	Next state
I		a		II
I		A		II
II		a		II
II		A		II
II		N		III

9.3	The constructed DFA

The DFA obtained for the above syntax tree would look like :

a|A

II
I
a|A
N
III

This DFA represents the regular expression provided as a specification (i.e. pattern to be matched) in the first rule of the token simulator program in section 9. When the DFA is in the final state i.e. III, then a corresponding action is executed as instructed in the lex.yy.c file. The constructed DFA is simulated using a simulation algorithm.

10	The DFA simulation algorithm

The working of the constructed DFA is simulated using the following algorithm.

DFA_simulator()
current_state = start_state
c = get_next_char()
while(c != EOF)
current_sate = transition(current_state , c)
 c = get_next_char()
if(current_state ∈ Final_states)
/*ACCEPT*/
else
/*REJECT*/

The information about all the transitions made by the DFA can be obtained from the decision table (generally a two dimensional matrix) through the transition() function.

11	Using the generated lexical analyzer

The generated lex.yy.c file is the code for the scanner. This is compiled using a C compiler and the generated object file (the executable scanner) is executed. LEX is just a tool which helps generate a smart scanner in C.
The lexical analyzer only checks for recognizable pattern sequences in the source program and produces an output of tokens (fed to the parser) , it cannot be used to check for syntax. Syntax analysis is done by the parser. The parser is built using YACC , a parser generator. YACC obtains the tokens from LEX through yylex() and the associated attributes from yylval, which it uses for parsing and rest of the the compilation process. In this case, the programmer need not call yylex() in the LEX program, it is automatically called by YACC to read the tokens. The parser , when given an input source program obtains all the tokens from the lexical analyzer and checks for correctness of the syntax. Hence, the next step towards compiling a given source program would be to build a parser.

12	References

For further details on the topics covered in this document, the reader may refer to the following books :
- Compilers : Principles,Techniques and Tools by Alfred V.Aho, Monica S. Lam, Ravi Sethi and Jeffrey D.Ulman .
- Modern Compiler Implementation in C by Andrew W.Appel
- Flex & Bison by John Levine